# Rotoscope project
General rotation code rev_1
#define dirPin 9
#define stepPin 6

void setup() {
// put your setup code here, to run once:
  Serial.begin(9600);
  pinMode(stepPin,OUTPUT);
  pinMode(dirPin,OUTPUT);
  digitalWrite(dirPin, LOW);
  Serial.println("initialize..."

}

void loop() {
  // put your main code here, to run repeatedly:
  Serial.println("working...");
  digitalWrite(stepPin, HIGH);
  delayMicroseconds(50);
  digitalWrite(stepPin, LOW);
  delayMicroseconds(50);

}

Maximum speed that can be achieved from the motor
// Define pin connections
const int stepPin = 3;  // Step pin connected to Arduino digital pin 3 (PUL+)
const int dirPin = 4;   // Direction pin connected to Arduino digital pin 4 (DIR+)
const int enablePin = 5; // Enable pin connected to Arduino digital pin 5 (ENA+)
void setup() {
  // Set the step, direction, and enable pins as outputs
  pinMode(stepPin, OUTPUT);
  pinMode(dirPin, OUTPUT);
  pinMode(enablePin, OUTPUT);
  // Enable the stepper driver
  digitalWrite(enablePin, LOW);  // Enable pin LOW (active low)
  // Initialize serial communication for monitoring (optional)
  Serial.begin(9600);
}
void loop() {
  // Set the direction (CW or CCW)
  digitalWrite(dirPin, HIGH);  // Set direction pin to HIGH for clockwise rotation
  // digitalWrite(dirPin, LOW); // Uncomment for counter-clockwise rotation
  //delay(1000);
  // Send a pulse to the step pin to move the motor one step
  digitalWrite(stepPin, HIGH);
  delayMicroseconds(200);
  // 200 is the max speed
  // switch on and oiff the supply at the time of uploading code
  digitalWrite(stepPin, LOW);
  delayMicroseconds(200);
  // You can add additional steps here if needed

}

Controlling the stepper with a button in single direction (changeable) speed and acceleration can be altered anytime in the code
#include <AccelStepper.h>

// Define stepper motor connections and other parameters
#define DIR_PIN 8 // Direction pin
#define STEP_PIN 9 // Step pin
// Initialize the stepper motor object
AccelStepper stepper(AccelStepper::DRIVER, STEP_PIN, DIR_PIN);
// Push button pin
#define BUTTON_PIN 2
// Variables to store button state
int buttonState = 0;
int lastButtonState = 0;

void setup() {
  // Setup the button pin as input
  pinMode(BUTTON_PIN, INPUT_PULLUP); // Use internal pull-up resistor
  // Set initial speed and acceleration
  stepper.setMaxSpeed(1000000); // Set maximum speed
  stepper.setAcceleration(1000); // Set acceleration

  // Begin serial communication (for debugging, optional)
  Serial.begin(9600);
}

void loop() {
  // Read the push button input
  buttonState = digitalRead(BUTTON_PIN);
  // If the button state has changed
  if (buttonState != lastButtonState) {
    // Check if the button is pressed (buttonState is LOW when pressed due to INPUT_PULLUP)
    if (buttonState == LOW) {
      // Toggle motor direction by changing target position
      stepper.move(100000); // Move 1000 steps in the current direction
    }
    delay(100); // Debounce delay
  }

  // Update the stepper motor
  stepper.run();
  // Store the current button state in the last button state variable
  lastButtonState = buttonState;
}

Final code
#include <AccelStepper.h>

// Define stepper motor connections and other parameters
#define PUL_PIN 12 // Direction pin
#define DIR_PIN 13 // Step pin

// Initialize the stepper motor object
AccelStepper stepper(AccelStepper::DRIVER, DIR_PIN, PUL_PIN);

// Push button pin
#define BUTTON_PIN 4
#define LIMIT_PIN 5

// Variables to store button state
int buttonState = 0;
int lastButtonState = 0;

int limitState = 0;
int lastlimitState = 0;

void setup() {
  // Setup the button pin as input
  pinMode(BUTTON_PIN, INPUT_PULLUP); // Use internal pull-up resistor
  pinMode(LIMIT_PIN, INPUT_PULLUP); // Use internal pull-up resistor

  // Set initial speed and acceleration
  stepper.setMaxSpeed(10000); // Set maximum speed
  stepper.setAcceleration(1000); // Set acceleration
  //stepper.setSpeed(100000);

  // Begin serial communication (for debugging, optional)
  Serial.begin(9600);
}

void loop() {
  // Read the push button input
  buttonState = digitalRead(BUTTON_PIN);

   //stepper.runSpeed();

  // If the button state has changed
  if (buttonState != lastButtonState) {
    // Check if the button is pressed (buttonState is LOW when pressed due to INPUT_PULLUP)
    if (buttonState == LOW) {
      // Toggle motor direction by changing target position
      //stepper.setSpeed(100000);
      stepper.move(1000); // Move 1000 steps in the current direction
    }
    delay(500); // Debounce delay
  }

  limitState = digitalRead(LIMIT_PIN);
  // Read the push limit input
  if (limitState != lastlimitState) {
    // Check if the button is pressed (buttonState is LOW when pressed due to INPUT_PULLUP)
    if (limitState == LOW) {
      // Toggle motor direction by changing target position
      //stepper.setSpeed(-1000);
      stepper.move(-4000); // Move 1000 steps in the opposite direction
    }
    delay(500); // Debounce delay
  }

  // Update the stepper motor
  stepper.run();

  // Store the current button state in the last button state variable
  lastButtonState = buttonState;
  lastlimitState = limitState;
}